## Slide 1
APURVA PANIDHAR 2210411204
DN GAURAV RAJ 1210411114
PATLURI SRI CHAITANYA 2210411246
SAHITHI MANAM 2210411252
UNDER THE GUIDANCE OF:
Mr. B. SAMMUNAYAK M.Tech
ASSISTANT PROFESSOR
GITAM UNIVERSITY
HYDERABAD CAMPUS
VOICE RECOGNITION AND EMAIL BASED HOME AUTOMATION SYSTEM USING RASPBERRY PI

## Slide 2: VOICE RECOGNITION
Voice or speech recognition is the ability of a machine or program to receive and interpret dictation, or to understand and carry out spoken commands.

## Slide 3: VOICE RECOGNITION SYSTEM
Enables user to control home appliances with voice commands when in the home
Implies that the system can only take dictation and not understand words
So you talk and your electronics listen!

## Slide 4: POCKETSPHINX
PocketSphinx is a lightweight speech recognition engine.
A version of Sphinx that can be used in embedded systems like those based on an ARM processor.
Incorporates features such as fixed-point arithmetic and efficient algorithms for GMM computation.

## Slide 5: FEATURES OF POCKETSPHINX
All the processing takes place on the Raspberry Pi, so it is capable of being used offline.
It supports real time speech recognition.
Pocketsphinx is resource-efficient.
Pocketsphinx supports many languages out-of box. It supports US English, Chinese, French, Russian, German, Dutch and more without need to train anything.
Pocketsphinx is completely free software.
Available bindings for several programming languages are present.

## Slide 6: INSTALLATION
Setup and properly configure ALSA[Advanced Linux Sound Architecture].
Check your microphone is visible or not and if on which usb extension.
Download sphinxbase latest and extract it.
Download pocketsphinx and extract it.
Run it.

## Slide 7: PYTHON CODE FOR TESTING VOICE RECOGNITION
#!/usr/bin/python
import time
import datetime
import math
import sys, select, subprocess
import os
proc = subprocess.Popen(['sh', '-c', 'pocketsphinx_continuous -adcdev hw:1,0 -nfft 2048 -samprate 48000 2>/dev/null'],stdout=subprocess.PIPE)
while True:
line = proc.stdout.readline()
if line != '':
output = line.rstrip()
print output
if (len(output.split("john"))>1):
os.system("sudo python home/pi/on.py")
if (len(output.split(“off"))>1):
os.system("sudo python home/pi/off.py")
if (len(output.split(“hi"))>1):
os.system("sudo python home/pi/five.py")
else:
break

## Slide 9: MODES OF OPERATION
Using the voice recognition software, we have operated the LED in 3 modes. They are:
1] On Mode
2] Off Mode
3] Blink Mode

## Slide 10: ON MODE

## Slide 11: OFF MODE

## Slide 12: BLINK MODE

## Slide 13: RESULTS 1-ON MODE

## Slide 15: RESULTS 2-OFF MODE

## Slide 17: RESULTS 3-BLINK MODE